# Calc Areas
## Description
This functor calculates the area of each source feature.
## Inputs
Name	Type	Description
Categorical Map	Categorical Map	Map containing classes or categories.

## Output
Name	Type	Description
Areas	Table	Area of each map category in cells, hectares and square meters.

## Group
Map Algebra
## Notes
Only the areas corresponding to class or categories defined in the input map header are calculated.
If the cell dimensions are represented using degrees, the areas in hectares and square meters becomes an approximation. All cells are always supposed to be of the same size.
The table containing the resulting area has the following format.
Column Name	Key or Data?	Column Type	Description
“Category”	Key	Real	Category in the feature map
“Area_In_Cells”	Data	Real	Area of corresponding category in cells
“Area_In_Hectares”	Data	Real	Area of corresponding category in hectares
“Area_In_Square_Meters”	Data	Real	Area of corresponding category in square meters

## Internal Name
CalcAreas