# Projection Type
Represents a map projection.
## GUI Editor
## EGO Script
A constant representing a projection in a EGO Script can be defined in two different ways:
### Using ERMapper parameters
[| "COORDINATE_TYPE", "ERMAPPER_PROJECTION", "ERMAPPER_DATUM", "ERMAPPER_UNIT" |]

All parameters are case-insensitive and must be surrounded by double quotes.
Example:
[| "LATLONG", "GEODETIC", "WGS84", "METERS" |]

### Using a WKT (Well-Known Text) description
[| "COORDINATE_TYPE", WKT_PROJECTION |]

The syntax used to the represent the WKT_PROJECTION can be found here.
It is worth nothing that only the COORDINATE_TYPE must be surrounded by double quotes.
Example:
[| "LATLONG", PROJCS["unnamed", GEOGCS["WGS 84", DATUM["WGS_1984", SPHEROID["WGS 84",6378137,298.257223563, AUTHORITY["EPSG","7030"]], TOWGS84[0,0,0,0,0,0,0], AUTHORITY["EPSG","6326"]], PRIMEM["Greenwich",0, AUTHORITY["EPSG","8901"]], UNIT["degree",0.0174532925199433, AUTHORITY["EPSG","9108"]], AUTHORITY["EPSG","4326"]], PROJECTION["Transverse_Mercator"], PARAMETER["latitude_of_origin",0], PARAMETER["central_meridian",90], PARAMETER["scale_factor",0.9996], PARAMETER["false_easting",500000], PARAMETER["false_northing",-2000000], UNIT["METERS",1]]] |]

A COORDINATE_TYPE is also case-insensitive and must be represented using keywords “en” (Easting/Northing), “latlong” (Latitude/Longitude) and “none”. The latter can be used to automatically derive the coordinate type based on the projection parameters.
## Automatic Conversions
Converted from: Map Type and Categorical Map Type.
Converted to: None.