# Calc Distance Map
## Description
This functor calculates a map representing the frontage distance (in meters) between a cell and the closest cell of a certain category specified in the “Categorical Map” input.
## Inputs
Name	Type	Description
Categorical Map	Categorical Map	Map of classes or categories. Null value cells on this map will produce the same null value cells on the resulting distance map. Data cell type of this map must be “Signed 32 Bit Integer” or an error will be reported.
Categories	Int Set	List of categories. Distance maps are calculated for these categories. Each category corresponds to a layer “distance_to_i” where i is an identifier of a category on the input map.

## Optional Inputs
Name	Type	Description	Default Value
Cell Type	Cell Type	Data cell type.	Signed 32 Bit Integer
Null Value	Int	Null value of the distance map.	-2147483648
Truncate Distance	Bool	If true, distance values that exceed the greatest value of the output map will be truncated, instead of informing an error.	False.

## Outputs
Name	Type	Description
Distance	Map	The distance map. The distances are represented in meters. Map format has the same dimensions of the “Categorical Map”.

## Group
Map Algebra
## Notes
The calculated distance is the Euclidean distance and the unit used is the meter.
## Internal Name
CalcDistanceMap