# Create Map
## Description
This functor creates an empty map using the given parameters.
## Inputs
Name	Type	Description
Lines	Positive Int	Number of lines.
Columns	Positive Int	Number of columns.
Cell Type	Cell Type	Data cell type.
Null Value	Null Value	Null value.
Projection	Projection	Map projection.
Cell Width	Double	Cell width.
Cell Height	Double	Cell height.
Registration Coordinate Y	Double	The registration coordinate Y. The unit used to represent the registration coordinate is based on the projection assigned.
Registration Coordinate X	Double	The registration coordinate X. The unit used to represent the registration coordinate is based on the projection assigned.

## Optional Inputs
Name	Type	Description	Default Value
Registration Cell Y	Positive Int	The line of the registered coordinate. The line 1 is the topmost line.	1
Registration Cell X	Positive Int	The column of the registered coordinate. The column 1 is the leftmost column.	1
Create As Sparse	Bool	If true, this flag forces the map to be created as a sparse raster set. Sparse raster set stores only non-null value cells, minimizing storage memory in detriment of access time.	False

## Outputs
Name	Type	Description
Map	Map	The output map.

## Group
Map Algebra
## Notes
All map cells are initialized with the specified null value.
## Internal Name
CreateMap