# Calc Histogram
## Description
This functor calculates a histogram from a map.
## Inputs
Name	Type	Description
Map	Map	Any map

## Optional Inputs
Name	Type	Description	Default Value
Interval Width	Double	The width of the histogram interval.	1.0
Cumulative	Bool	If true, the calculated histogram is cumulative.	False
Relative	Bool	If true, the values in the histogram are normalized by the total number of occurrences.	False

## Outputs
Name	Type	Description
Histogram	Lookup Table	The calculated histogram.

## Notes
It also possible to calculate a histogram relative to the cumulative values. To do this, set both input flags (“Cumulative” and “Relative”).
When the “Interval Width” is different from one, the input values are remapped according to the expression below to speed up the calculation.
, where value´ is the resulting value, value is the value present in the input map and width is the width of the interval.
Because of the remapping, the lower and upper limits of the resulting histogram can be lower and greater, respectively, than the lower and upper limits of the input map.
## Group
Statistics
## Internal Name
CalcHistogram