# Regional Map
## Description
This functor stores all of the regional maps produced within the Region Manager container.
## Inputs
Name	Type	Description
Global Map Name	Name	Name for the regional maps.
Regional Map	Map	Any map passed as input.
Region Id	Int	Region Id.[1)]
Region Manager	Region Manager	This is internally linked by the Region Manager container.1)
[1)] Since Dinamica 1.9.x, this input is no longer optional

## Outputs
## Group
Region
## Notes
This structure stores all regional maps created or modified during the execution of the Region Manager and its enveloped containers. These maps can be merged afterwards by the Merge Regional Maps functor.
## Internal Name
RegionalMap