# Calculate R Expression
## Description
This is a container functor that calls R externally with the user-defined expression. Like the other calculator functors, data is connected through hook functors placed inside its {{ … }} block.
## Inputs
Name	Type	Description
Expression	Code	The expression that will run on R. Code values cannot be written as plain text constants in EGO Script — see Writing the expression in EGO Script below.
Treat Warning As Errors	Boolean Value Type	Warnings raised by the R script will be treated as errors.

## Optional Inputs
None.
## Outputs
Name	Type	Description
result	Struct	A struct containing the output values generated by the expression.

## Notes
### Expression inputs
Data is passed into the expression through hook functors placed inside the container's {{ … }} block — the same verbose form hook mechanism used by the calculator functors. Hooks can be added using the Create a hook button on the functor bar, or by dragging them in individually.
- Tables and lookup tables → Number Table → available in R as t1, t2, …, t100
- Scalar values → Number Value → available as v1, v2, …, v100
- Strings → Number String → available as s1, s2, …, s100
Maps cannot be connected — this functor has no cell context. There is no shorthand notation; see Calculate Functors — Complete Operator Documentation for the general hook mechanism and syntax.
#### Tables and lookup tables
Lookup tables and tables require extra care, since each is transferred to R using a different representation.
A lookup table is transferred as a list with two columns, Key and Value. Each column is accessed with the $ operator:
# Access the third key and its corresponding value in lookup table t1 patchId <- t1$Key[3]; patchArea <- t1$Value[3];

A table is transferred as a DataFrame, with each column likewise accessed using $. Two conventions apply to tables in either direction:
- Key columns are marked by an asterisk (*) appended to their column name — this is the same convention used throughout Dinamica EGO's table representation (see Connecting Data Inputs). A key column can be Real or String, the same as any other column.
- Each column's type is inferred from its data, the same rule that applies to any table (see Constants): a numeric vector produces a Real column, a character vector produces a String column. R automatically converts string columns to Factors inside a data.frame, and a Factor is neither of those — Dinamica requires plain Character Vectors to infer String correctly. Always build tables with stringsAsFactors = FALSE to prevent this conversion.
For further detail on the underlying table representation, see External Communication.
### Expression outputs
Values are returned to Dinamica by calling one of the following functions from the R script. Every call requires an identifier as its first parameter — the name Dinamica uses to place the value into the output struct — and the value itself, which can be constructed inline, as in the examples below, or supplied as a variable:
Function	Output type	Notes	Example
outputDouble()	Real	Accepts any numeric value.	outputDouble(“myDouble”, 3.14)
outputNumberVector()	Tuple	Accepts any collection of numbers.	outputNumberVector(“myTuple”, c(1:10))
outputString()	String	Accepts any string value.	outputString(“myString”, “This is a string”)
outputLookupTable()	Lookup Table	Requires two number vectors of equal length — one for the keys, one for the values. Lookup tables are always Real-typed on both sides; there is no String option.	outputLookupTable(“myLUT”, c(1:10), c(1:10) * 10)
outputTable()	Table	Requires a table built with the data.frame function, using stringsAsFactors = FALSE as described above. Its optional second parameter (default 1) sets how many leading columns, from the left, are key columns.	outputTable(“myTable”, data.frame(State = c(“Massachusetts”, “Massachusetts”), City = c(“Boston”, “Chelsea”), Population = c(667137, 39398), stringsAsFactors = FALSE), 2)

### Retrieving outputs
CalculateRExpression returns a single Struct value (via its result output port) containing every value passed to an output*() function. To retrieve individual values from that struct, use the corresponding functor from the Integration group:
Functor	Retrieves
Extract Struct Number	A value passed to outputDouble()
Extract Struct Tuple	A value passed to outputNumberVector()
Extract Struct String	A value passed to outputString()
Extract Struct Lookup Table	A value passed to outputLookupTable()
Extract Struct Table	A value passed to outputTable()

Each functor takes two inputs: the Struct returned by CalculateRExpression, and the name of the entry to extract as a string constant.
### Installing packages
Packages are installed by calling dinamicaPackage(“packageName”) from within the expression — one call per package. Unlike Calculate Python Expression, there is no separate input port for listing packages; dinamicaPackage() is the only mechanism available.
dinamicaPackage(“packageName”) also acts as R's library() call: when the package name matches the name of the module to load, calling it both installs the package (if not already present) and loads it, in a single call.
dinamicaPackage("moments");

### Setup
There are two ways to run R scripts from CalculateRExpression — though only the local installation is available on Linux.
#### Dinamica EGO Enhancement Plugin
Windows only. Download and install the Dinamica EGO Enhancement Plugin. It contains everything needed to run R scripts inside Dinamica EGO, with no further configuration.
#### Local R installation
On Linux, this is the only option — Dinamica EGO always uses the R installation already present on the system. On Windows, it can be used as an alternative to the plugin. Either way, it requires:
- R installed on the machine, with the Rscript executable (Rscript.exe on Windows) present in its bin sub-folder.
- The Dinamica package for R installed and at its latest version.
On Windows, this alternative installation is selected in the Dinamica EGO GUI by going to Tools → Options → Integration tab and enabling Use alternative R installation for Calculate R Expression.
### Examples
The following examples use a consistent set of inputs:
- t1 — a lookup table of land cover patches, mapping Key (patch identifier) to Value (patch area)
- v1 — a scalar minimum area threshold
- s1 — a string giving the name to use for the threshold flag column
Compute the mean and total area across all patches, and report progress to the Message Log:
patchMean <- mean(t1$Value); patchTotal <- sum(t1$Value); print(paste("Processed", length(t1$Value), "patches")); outputDouble("meanArea", patchMean); outputDouble("totalArea", patchTotal);

Note: The print() call is visible in Dinamica EGO's Message Log, shown as a Result-level message. Log levels are ordered Unconditional, Error, Warning, Result, Info, Info2, Debug, Debug2 — messages printed from R are only shown when the Message Log level is set to Result or a more verbose level; at Unconditional, Error, or Warning they are suppressed.

Filter the lookup table down to patches whose area meets the threshold, and return the filtered lookup table:
aboveThreshold <- t1$Value >= v1; filteredKeys <- t1$Key[aboveThreshold]; filteredValues <- t1$Value[aboveThreshold]; outputLookupTable("filteredPatches", filteredKeys, filteredValues);

Build and return a table with one row per patch, including a column that flags whether each patch meets the threshold. The column's name is taken from the passed string s1 rather than being hard-coded:
patchFlags <- data.frame( PatchId = t1$Key, Area = t1$Value, MeetsThreshold = t1$Value >= v1, stringsAsFactors = FALSE ); names(patchFlags)[3] <- s1; outputTable("patchSummary", patchFlags, 1);

Install the moments package and use it to compute the skewness of the patch area distribution — a statistic not available in base R — then flag patches whose area is a statistical outlier:
dinamicaPackage("moments"); patchMean <- mean(t1$Value); patchStdDev <- sd(t1$Value); patchSkewness <- skewness(t1$Value); isOutlier <- abs(t1$Value - patchMean) > 2 * patchStdDev; outlierPatches <- data.frame( PatchId = t1$Key[isOutlier], Area = t1$Value[isOutlier], stringsAsFactors = FALSE ); outputDouble("meanArea", patchMean); outputDouble("stdDevArea", patchStdDev); outputDouble("skewnessArea", patchSkewness); outputTable("outlierPatches", outlierPatches, 1);

### Writing the expression in EGO Script
Like Calculate Python Expression, the Expression input is type Code, which is represented in the underlying script using base64 encoding — impractical to write or edit directly as a text constant. Instead, connect a String carrier functor containing the R expression text to the Expression port; its output is accepted wherever a Code value is expected. Since only this one output is needed, the carrier can be inlined directly into the call.
This limitation is specific to hand-written EGO Script. In the Dinamica EGO GUI, the Expression port has a dedicated code editor that edits the Code value directly — the String carrier workaround is only necessary when writing or editing the .ego file as text.
result := CalculateRExpression (String $"(
aboveThreshold <- t1$Value >= v1;
outputLookupTable("filteredPatches", t1$Key[aboveThreshold], t1$Value[aboveThreshold]);
)") .no {{
    NumberTable landCoverAreas 1;
    NumberValue minimumArea 1;
}};
filteredPatches := ExtractStructLookupTable result "filteredPatches";
## Group
Integration
## Internal Name
CalculateRExpression